## Slide 1: CS 211 Computer Architecture Lab (MIPS Assembly Programming) Sharad Sinha sharad@iitgoa.ac.in
  1

## Slide 2
System Calls allow your assembly language program to access system services like
  Printing to screen
  Taking input from user etc.
Can you answer why we need System Calls? (The previous point only tells what they do and not why we need them)
  System calls (implemented by syscall instruction in MIPS ISA) place processor in supervisor mode; your code is executed in user mode
  When system calls are made, an exception or interrupt is raised and a corresponding interrupt/exception service routine or handler (I/ESR) is executed.
  This I/ESR (written inside SPIM simulator in your case) brings functionality like printing to screen for you
  2
System Calls

## Slide 3
Table 1 in lab manual 2 :
  3
Support for System Calls in SPIM
Service | System Call Code | Arguments | Result
print integer | 1 | $a0 = value | (none)
print float | 2 | $f12 = float value | (none)
print double | 3 | $f12 = double value | (none)
print string | 4 | $a0 = address of string | (none)
read integer | 5 | (none) | $v0 = value read
read float | 6 | (none) | $f0 = value read
read double | 7 | (none) | $f0 = value read
read string | 8 | $a0 = address where string to be stored $a1 = number of characters to read + 1 | (none)
memory allocation | 9 | $a0 = number of bytes of storage desired | $v0 = address of block
exit (end of program) | 10 | (none) | (none)
print character | 11 | $a0 = integer | (none)
read character | 12 | (none) | char in $v0

## Slide 4
Sample code:
li $v0, <system call code> #load system call code in register v0
la $a0, <arguments> #load arguments in registes a0-a3 or f12 for floating point values
syscall # call syscall
Read the manual for more details and explanation
  4
How to use a System Call

## Slide 5
  5
Control flow operations
  Control Flow operations: beq, bne, bgez, bgtz, j, jr,
Instruction | Syntax | Meaning
Branch when equal | beq $rs , $rt, imm | Branch if ($rs==$rt)
Branch when not equal | bne $rs , $rt, imm | Branch if ($rs!=$rt)
Branch greater than or equal to zero | bgez $rs , imm | Branch if ($rs >=0)
Branch greater than zero | bgtz $rs , imm | Branch if ($rs >0)
Jump | j offset | Jump by offset words
Jump register | jr $ra | Jump to the content of $ra
Jump and link | jal offset | Jump by offset words and saves PC+4 to $ra
  For branch if taken, nPC=PC + 4 + (imm x 4)
For Jump, nPC={4 upper bits of PC},{26 offset bits}, and {00}