## Slide 1: CS 211 Computer Architecture
Lab 03

## Slide 2: Exception
Exception:
Unexpected change in control flow.
It can be synchronous or asynchronous.
Synchronous(traps): If it occurs at the same place every time a program is executed.
Asynchronous(interrupts): It occurs with no temporal relation to the program being executed.

## Slide 3: Exception Handlers
When an exception happens, the control is transferred to a different program named exception handler, written explicitly for the purpose of dealing with exceptions.
After the exception, the control is returned to the program that was executing when the exception occurred: that program then continues as if nothing happened.
An exception appears as if a procedure (with no parameters and no return value) has been inserted in the program.

## Slide 4: Exception Handlers
In MIPS, exception mechanism is handled by Coprocessor 0.
Processor operates in either user or kernel mode. User programs run in user mode. The CPU enters the kernel mode when an exception happens.
By MIPS register usage convention, registers $k0 and $k1 are reserved for the use of exception handlers.

## Slide 5: Coprocessor 0
Registers of Coprocessor 0 are as follows:
1. BadVAddr: Contains the invalid memory address caused by load, store, or fetch.
2. Status: Contains the interrupt mask and enable bits.
3. Cause: Contains the type of exception and any pending bits.
4. EPC: Contains the address of the instruction when the exception occurred.

## Slide 6: Instructions which access the registers of Coprocessor 0
Table 01

## Slide 7: Extended Assembler
An extended assembler creates a view that is a level higher than the assembly level. Many of the statements accepted by the extended assembler correspond to several machine instructions.
Eg1: mov d,s
This instruction moves the contents of source register s to destination register d
This instruction is translated into the following assembly instruction
Addu d,s,$zero
Eg2: li d, value
load register $d with the positive or negative integer "value". Value may be a 16 or a 32-bit integer.
This instruction is translated into the following assembly instruction
Ori d,$Zero,value